## Slide 1: Hardware: The CPU & Storage
Chapter 4
4

## Slide 2: Chapter Topics
UNIT 4A: Processing: The System Unit, Microprocessors, & Main Memory
4.1 Microchips, Miniaturization, & Mobility
4.2 Representing Data Electronically
4.3 Inside the System Unit: Power Supply, Motherboard, & Microprocessors
4.4 The Central Processing Unit & the Machine Cycle
4.5 Memory
4.6 Expansion Cards, Bus Lines, & Ports
UNIT 4B: Secondary Storage
4.7 Secondary Storage
4.8 Future Developments in Processing & Storage

## Slide 3
UNIT 4A: Processing: The System Unit, Microprocessors, & Main Memory
Electronic circuitry has remained basically the same over recent years.
A circuit is a closed path followed or capable of being followed by an electric current.
Vacuum tubes used wire circuits inside them to facilitate the flow of electrons.
Transistors have replaced vacuum tubes.

## Slide 4: 4.1 Microchips, Miniaturization, & Mobility

## Slide 5
The Since the early 1970s, microchips have gotten smaller and smaller yet more and more powerful and faster.
A transistor is a tiny electronic switch that can be turned “on” or “off” millions of times per second.
Transistors form part of an integrated circuit: all the parts of an electronic circuit embedded on a single silicon chip.
Integrated circuits are solid state (no moving parts).

## Slide 6
  Silicon: A semiconductor made of clay and sand.
  Semiconductor: A material whose electrical properties are intermediate between a good conductor and a nonconductor of electricity.
    Perfect underlayer for highly conductive,
    complex circuits.
    Microchips (Microprocessors) are made
    from semiconductors.
  Chip: A tiny piece of silicon that contains
  millions of microminiature integrated
  electronic circuits.
Chip

## Slide 7
Miniaturization
  Microchips
    Store and process data in electronic devices
  Microprocessors
    The miniaturized circuitry of an entire computer processor (“brain”) on a single chip
    Contains the central processing unit (CPU), which processes data into information
  The development of microchips and processors has enabled the development of small, mobile electronic devices.

## Slide 8
System Unit
  The case that contains the computer’s electronic components used to process data.
    PCs: Tower or desktop; monitor is separate.
    Laptops: Monitor is attached to the system unit, like a clamshell.
    Tablets: Usually includes a touch-screen interface.
    Smartphones: Handheld system units.

## Slide 9: 4.2 Representing Data Electronically

## Slide 10
Binary System: the basic data-representation method for computers uses just two numbers: 0 and 1, representing the off/on states of electricity or light pulses.
Data is represented in a computer by binary code.

## Slide 11
  All data and program instructions in the computer are represented as binary.
  Bit: each 0 or 1 is a bit
  Byte: a group of 8 bits = 1 character, digit, or other value
  Kilobyte (KB): 1,000 (1,024) bytes
  Megabyte (MB): 1 million (1,048,576) bytes
  Gigabyte (GB): 1 billion (1,073,741,824) bytes
  Terabyte (TB): 1 trillion (1,009,511,627,776) bytes
  Petabyte (PB): 1 quadrillion bytes
  Exabyte (EB): 1 quintillion bytes
Measuring Capacity

## Slide 12
Binary coding schemes assign a unique binary code to each character.
  ASCII (American Standard Code for Information Interchange)
    Requires 7 or 8 bits per character, depending on the version
    8-bit Extended ASCII provides 256 characters
    Commonly used for microcomputers
  Unicode
    Requires 16 bits per character
    Handles 65,536 characters—used for Chinese and Japanese
  EBCDIC (Extended Binary Coded Decimal Interchange Code)
    Requires 8 bits per character
    Used for IBM mainframes

## Slide 14
Machine Language: The computer’s “native language”
  A binary-type programming language (0s and 1s) built into the CPU that is run directly by the computer.
  Each CPU type has its own machine language; thus each computer’s machine language is brand-dependent.
  Language Translators: The computer’s system software converts higher-level language instructions and data into machine language so that the processor can “understand” what to do.

## Slide 15: 4.3 Inside the System Unit
Power Supply, Motherboard, & Microprocessors

## Slide 16
Terms
Definitions
Bay
Power Supply
Surge Protector
UPS
Motherboard
Microprocessor
Chipset
Opening in the computer cabinet used for the installation of electrical equipment.
This converts AC to DC to run the computer.
Protects the computer from being damaged by power spikes. Plug your computer into one.
Uninterruptible Power Supply. Battery-operated device that provides power for a limited time when there is a blackout.
Main system board of the computer (also systemboard).
Miniaturized circuitry of a computer processor.
Groups of interconnected chips on the motherboard that control information flow between the microprocessor and other system components connected to the motherboard.

## Slide 17
One View of a Motherboard

## Slide 18
Another View of a Motherboard

## Slide 19
A Mac motherboard
Hard drive
Expansion cards
Motherboard
CD drive
Power supply
RAM slots

## Slide 21
Traditional microcomputer microprocessors are Intel and AMD.
Multicore processors (2, 4, 6, 8) have more than one
processor “core” on a single silicon chip, which
allows computers to run faster.
Special processors are made for portable devices.
A graphics processing unit (GPU) is a specialized processor used to manipulate three-dimensional (3-D) computer graphics.

## Slide 22
Processing Speeds
  Every microprocessor contains a system clock, which controls how fast all the operations within a computer take place (the chip’s processing speed).
  Older CPU processing speeds are in megahertz.
    1 MHz = 1 million cycles per second
  Current CPU processing speeds are in gigahertz.
    1 GHz = 1 billion cycles per second
  The faster a CPU runs, the more power it consumes, and the more heat it generates.

## Slide 23: 4.4 The Central Processing Unit & the Machine Cycle

## Slide 24
The CPU, for central processing unit, is the “brain” of the computer; it follows the instructions of the software (program) to manipulate data into information.
The CPU consists of two parts—(1) the control unit and (2) the arithmetic/logic unit (ALU), both of which contain registers, or high-speed storage areas.
All are linked by a kind of electronic “roadway” called a bus.

## Slide 26
The control unit deciphers each instruction stored in the CPU and then carries out the instruction. It directs the movement of electronic signals between main memory and the arithmetic/logic unit. It also directs these electronic signals between main memory and the input and output devices.
For every instruction, the control unit carries out four basic operations, known as the machine cycle. In the machine cycle, the CPU (1) fetches an instruction, (2) decodes the instruction, (3) executes the instruction, and (4) stores the result (see next slide)..

## Slide 27
Each time the central processing unit executes an instruction, it takes a series of steps. The complete series of steps is called a machine cycle.

## Slide 28
The arithmetic/logic unit (ALU) performs arithmetic operations and logical operations and controls the speed of those operations.
Arithmetic operations are the fundamental math operations: addition, subtraction, multiplication, and division.
Logical operations are comparisons--the ALU compares two pieces of data to see whether one is equal to ( = ), greater than (>), greater than or equal to ( >= ), less than (<), less than or equal to ( <= ), or not equal to ( ≠ ) the other.

## Slide 29
The control unit and the ALU also use registers, special CPU areas that enhance the computer’s performance.
Registers are high-speed storage areas that temporarily store data during processing. They may store a program instruction while it is being decoded, store data while it is being processed by the ALU, or store the results of a calculation.
All data must be represented in a register before it can be processed.
The number of registers that a CPU has and the size of each (number of bits) help determine the power and speed of a CPU.

## Slide 30
Buses are electrical data “roadways” through which bits are transmitted within the CPU and between the CPU and other components of the motherboard.
In most computers, the bus width is the same as the computer’s word size, the number of bits that the processor can process at any one time. The more bits in a word, usually the faster the computer. A 32-bit-word computer will transfer data within each microprocessor chip in 32-bit chunks. A 64-bit-word computer is faster, transferring data in 64-bit chunks at a time. (Most, but not all, 32-bit software will run on a 64-bit system, but 64-bit software will not run on a 32-bit system.)

## Slide 31: 4.5 Memory

## Slide 32
Memory
  Two type of storage: primary and secondary.
    Primary storage = “memory,” “main memory,” “RAM”; this type of memory is temporary and volatile.
    Secondary storage = hard disks and flash memory units; this type of memory is relatively permanent and nonvolatile.

## Slide 33
Memory Chips
RAM
ROM
CMOS
Flash
Explanation
Random Access Memory chips are volatile and hold:
  Software instructions
  Data before & after the CPU processes it
Read Only Memory
  Cannot be written on or erased without special equipment
  Are loaded at factory with fixed (permanent) start-up instructions (BIOS), that tell the computer how to load the operating system
Complementary Metal Oxide Semiconductor
  Powered by a battery
  Contains time, date, calendar, boot password
Nonvolatile memory that can be erased and reprogrammed more than once
  Doesn’t require a battery
  Used in newer PCs for BIOS instructions

## Slide 34
Speeding up Processing: Cache
  The CPU works much faster than RAM, so it often must wait for information
  Cache temporarily stores instructions and data that the processor uses frequently to speed up processing
      Level 1 cache is part of the microprocessor
        Holds 8 to 128 KB
        Faster than Level 2 cache
      Level 2 cache is external cache
        Holds 64 kb to 16 MB
      Level 3 cache is on the motherboard
        Comes on very high-end computers
        Holds 2 to 8 MB

## Slide 35
Virtual Memory—also used to speed up processing.
  This type of memory is unused hard disk or optical (CD) space that the processor uses to extend the capacity of RAM.
  The processor goes first to L1 cache, then L2 cache, then RAM, then virtual memory.
  Each type of memory is slower than its predecessor.

## Slide 36: 4.6 Expansion Cards, Bus Lines, & Ports

## Slide 37
Expansion cards plug into slots on the motherboard that are connected by buses to ports that the user can access.
Expansion cards are circuit boards that provide more memory or that control peripheral devices (for graphics, sound, video, network interface, wireless connection, etc.).
Buses connect the expansion cards to ports.
A port is a connecting socket or jack on the outside of the computer unit or device into which are plugged different kinds of cables that connect peripheral devices.

## Slide 38
Expansion Cards: If a computer uses closed architecture, no expansion cards can be added; if the computer uses open architecture, expansion cards can be inserted in expansion slots inside the computer, connected to the motherboard.

## Slide 39
An expansion bus is not the same as the frontside bus:
Frontside bus: The bus that connects the CPU within itself and to main memory.
Expansion bus: Buses that connect the CPU with expansion slots on the motherboard and thus via ports with peripheral devices.

## Slide 40
Types of expansion buses:
PCI: High-speed bus that has been widely used to connect PC graphics cards, sound cards, modems, and high-speed network cards.
PCI Express: Doubles the speed of the original PCI bus . PCIe is the latest standard for expansion cards available on mainstream personal computers.
Accelerated Graphics: Transmits data at twice the speed of a PCI bus and is designed to support video and 3-D graphics.
Universal Serial Bus (USB): Does away with the need to install cards in expansion slots. USB devices can connect one to another outside the system unit, and then the USB bus connects to the PCI bus on the motherboard.
Firewire: Resembles the USB bus but is used for more specialized purposes, such as to connect audio and video equipment to the motherboard.

## Slide 41
Port Type
Serial port
Parallel port
USB port
Description
Used to transmit data slowly over long distances
  Sends data sequentially, one bit at a time
  Used to connect older keyboards, mouse, monitors, dial-up modems
For transmitting data quickly over short distances
  Transmits 8 bytes simultaneously
  Connects printers, external disks, tape backups
Universal Serial Bus high-speed hardware standard for interfacing peripheral devices, such as scanners and printers, to computers without a need for special expansion cards or other hardware modifications to the computer. USB is replacing many varieties of serial and parallel ports.
A port is a socket for some kind of plug, of which there are many types.

## Slide 42: Specialized Expansion Ports
Port Type
FireWire Intended for multiple devices working with lots of data and requiring fast transmission speeds, such as DVD drives, digital video cameras, and gaming consoles.
Ethernet Supports a network standard for linking a wired local area network and connecting it to a DSL or a cable modem for high-speed Internet access.
Graphics Connects digital monitors and multimedia digital devices, such as TVs and DVD players.
eSATA External Serial Advanced Technology Attachment; allows the attachment of an eSATA hard disk, which has fast data transmission speeds.
Bluetooth Connects devices that use short-range radio waves that transmit up to 30 feet.
IrDA Transfers data via infrared light waves between directly aligned devices, as between a smartphone and a desktop computer.
HDMI High-Definition Multimedia Interface; carries both video and audio signals and is used for connecting HDTVs, DVD players, and game consoles to computers, laptops, and other devices.
MIDI Musical Instrument Digital Interface; used to connect electronic musical instruments to a sound card that converts the signals to digital instructions that can be saved or manipulated.

## Slide 45
UNIT 4B:
Secondary storage hardware includes devices that permanently hold data and information as well as programs.
Online, or cloud, storage is also available, but we still use secondary storage hardware.

## Slide 46: 4.7 Secondary Storage

## Slide 47
Hard Disks: Still the major secondary-storage device for desktop/tower computers.
  Thin, rigid metal, glass, or ceramic platters covered with a substance that allows data to be held in the form of magnetized spots.
    The more platters there are, the higher the drive capacity.
    Store data in tracks, sectors, and clusters.
    Formatting creates a file allocation table that maps files to clusters.
    Drive heads ride on .000001” cushion of air, and can crash!
    Important data should always be backed up!
read/write head

## Slide 49
Hard Disks (continued)
  Hard Disk Types:
    Nonremovable hard disk – Also known as a fixed disk; is housed in the microcomputer system unit and is used to store nearly all programs and most data files. Usually consists of several metallic or glass platters, from 1 to 5.25 inches (most commonly 3.5 inches) in diameter, stacked on a spindle, with data stored on both sides. Read/write heads, one for each side of each platter, are mounted on an access arm that moves back and forth to the right location on the platter.
    External hard disk – Freestanding disk drive (portable); usually connected via USB.
    RAID – redundant array of independent disks; for large computer systems.

## Slide 51
Optical Disks
  CDs (compact disks) and DVDs (digital versatile/video disks) are optical disks.
  DVDs hold more data then CDs do.
  Data is written and read using lasers, not a disk read/write head.
    CD-ROM is Compact Disk Read-Only Memory; content is prerecorded.
    CD-R (compact disk-recordable) is used for recording only once.
    CD-RW (compact disk-rewritable)is an erasable optical disk that can both record and erase data over and over again.

## Slide 52
Optical Disks (continued)
  DVD is a CD-style disk with extremely high capacity.
  DVD-R (DVD-recordable) is used for recording only once.
  DVD-RW, DVD-RAM, DVD+RW are reusable DVDs.
  Blu-ray is an optical-disk format used to record, rewrite, and play back high-definition (HD) video, as well as to store large amounts of data.

## Slide 53
Flash & Solid-State Storage
Flash memory and solid-state memory have become the most important form of mobile secondary storage.
Disk drives (hard disks or CDs/DVDs) all involve some moving parts—and moving parts can break. By contrast, flash memory has no moving parts; it is “solid state.” Flash memory is also nonvolatile—it retains data even when the power is turned off.
Flash memory media are available in three forms:
  Some tablets, laptops, desktops, and servers feature a solid-state drive (SSD), which uses flash memory to store data, instructions ,and information.
  Flash memory cards, or flash RAM cards, are removable and reusable storage media that are inserted into a flash memory slot in a digital camera, notebook, smartphone, or other mobile device.
  A USB flash drive consists of a finger-size module of reusable flash memory that plugs into the USB ports of nearly any microcomputer.

## Slide 54
Smart Card: pocket-size card with integrated circuits.
  Resembles a credit card but contains a microprocessor and memory chips
    May function on three levels: credit, debit, and/or personal information
    Storage capacity: around 10 MBs
    Contact smart cards
      Must be swiped through card readers
      Can wear out from use
    Contactless smart cards
      Read when held in front of a low-powered laser

## Slide 55
Online Secondary Storage (Cloud Storage)
  Allows you to use the Internet to back up your data
    Sign up with a vendor and receive access to software and applications that allow you to upload your data to that company’s server

## Slide 56: 4.8 Future Developments in Processing & Storage

## Slide 57
Nanotechnology
Optical computing
DNA computing
Quantum computing
Better batteries
Description of Processing Technology
Tiny machines work at a molecular level to make nanocircuits
Uses lasers and light, not electricity
Uses strands of synthetic DNA to store data
Based on quantum mechanics and stores information using particle states
Wireless charging of batteries, longer-lasting batteries

## Slide 58
Future Developments in Secondary Storage
  Higher-density disks
    Perpendicular recording technology: stacking magnetic bits vertically on the surface of a platter (instead of horizontally, as usual)
    Molecular electronics– storage at the subatomic level

## Slide 59: Hardware: Input & Output
Chapter
5

## Slide 60: Chapter Topics
UNIT 5A: Input Hardware
5.1 Keyboards
5.2 Pointing Devices
5.3 Source Data-Entry Devices
5.4 The Future of Input
UNIT 5B: Output Hardware
5.5 Softcopy Output: Display Screens
5.6 Hardcopy Output: Printers
5.7 Mixed Output: Sound, Voice, & Video
5.8 The Future of Output
5.9 Quality of Life: Health & Ergonomics

## Slide 61
Input Hardware
  Devices that translate data into a form the computer can process
  Translates words, numbers, sounds, and pictures into binary 0s and 1s (off or on electrical signals or light pulses)
Output Hardware
  Devices that translate information processed by the computer into a form humans can understand
  Translates binary code into words,
  numbers, sounds, and pictures

## Slide 62
UNIT 5A: Input Hardware
The three major types of input hardware are keyboards, pointing devices, and source data-entry devices.

## Slide 64: 5.1 Keyboards

## Slide 65
Keyboards: convert letters, numbers,
and characters into electrical signals
  English keyboards differ from foreign language keyboards
How keyboards work:
  You press a key
  This interrupts the current flowing through the circuits
  Processor determines where the break occurs
  It compares the location of the break with the (x,y) character map for the language on the keyboard’s ROM chip
  A character is stored in keyboard memory
(continued)

## Slide 66
  Keyboards (continued)
    The character is then sent to PC as a data stream via wire or wireless connection
    OS interprets its own operating-system-specific commands and sends the others to the application for interpretation
    Most keyboards are QWERTY – named for the first six letters on the top left of the keyboard.
    Keyboards are either tactile (physical) or touch screen (virtual)

## Slide 67
Keyboard types
    104 – 108 keys desktop standard
    80 – 85 keys for laptops
    Wired
    Connect to CPU via a serial or USB port
  Wireless use either
    IR (infrared) technology
    Radio Frequency (RF) technology

## Slide 68
Terminal Types
  Dumb Terminals
    a.k.a. Video Display Terminal (VDT)
    Has display screen and keyboard
    Can do input and output only – no data processing
  Intelligent Terminals
    Has screen, processor, keyboard, and memory
    Can perform some independent functions
    Automated teller machine; point-of-sale terminal; mobile data terminal

## Slide 69: 5.2 Pointing Device

## Slide 70
Pointing devices include the mouse and its variants, the touch screen, and various forms of pen input.
Pointing devices control the position of the cursor or pointer on the screen and allow the user to select options displayed on the screen.
  Mouse is the principal pointing device.
    Mechanical mouse: a ball inside the mouse touches the desktop surface and rolls with the mouse.
    Optical mouse: uses laser beams and special chips to encode data for the computer.
    The mouse controls the mouse pointer on the screen – for example, an arrow, rectangle, pointing finger.
    When the mouse pointer changes to an I-beam, that indicates that text can be entered.
    The mouse has one to five buttons, used for various functions, such as clicking on and dragging items on the screen.

## Slide 71
Pointing Devices (continued)
  Trackball
    A movable ball mounted on top of a stationary device
    Good for locations where a mouse can’t move around enough
  Touchpad
    To use: slide your finger over this small flat surface
    Click by tapping you finger on the surface
    May require more practice to use than a mouse
    Used on laptops
  Pointing stick
    Located between the keys on a laptop keyboard, a pointing stick is a pressure-sensitive device that allows the user to control the pointer by directing the stick with one finger.

## Slide 72
Pointing Devices (continued)
  Touch Screens
    A video display screen sensitized to receive input from a finger touch.
    Used in ATMs, information, kiosks, reservation kiosks, voting machines, cellphones, tablets, and e-books.
    Multitouch Screens
    Display screens that allow two or more fingers or other gestures such as pinching motions to be recognized as input at any one time. It allows pinching and stretching gestures on the screen to control zooming.
  Pen input
    Uses a pen-like stylus for input.
    Uses handwriting recognition to translate cursive writing into data (handwriting recognition).

## Slide 73
Pointing Devices (continued)
  Light pen
    A light-sensitive penlike device that uses a wired connection to a computer terminal
    Bring the pen to the desired point on the display screen and press a button to identify the screen location
    Used by graphics artists, engineers, and in situations that require covered hands
  Digitizer
    Uses an electronic pen or puck to convert drawings
    and photos to digital data
    Digitizing tablets are often used in architecture

## Slide 74
Pointing Devices (continued)
  Digital Pen
    Writing instrument
    Writers can write on paper
    A tiny camera in the pen tip captures the writing
    A microchip in the pen converts the pen to digital ink
    The writing is sent as an image file to the computer
    Some versions require special paper

## Slide 75: 5.3 Source Data-Entry Devices

## Slide 76
Scanning & Reading Devices—Source data-entry devices that create machine-readable data and feed it directly into the computer (no keyboard is used)
  Scanners
    Use light-sensing equipment to translate images of text, drawings, and photos into digital form
    Image scanners are used in electronic imaging
    Resolution refers to the image sharpness, measured in dots per inch (dpi)
    Flatbed scanners work like photocopiers – the image is placed on the glass surface, then scanned
    Other types are sheet-fed, handheld, and drum

## Slide 77
  Bar-Code Readers (source data entry)
    Photoelectric (optical) scanners that translate bar code symbols into digital code
      The digital code is then sent to a computer
      The computer looks up the item and displays its name and associated information
    Bar code types
      1D (regular vertical stripes) holds up to 16 ASCII characters
      2D (different-sized rectangles) can hold 1,000 to 2,000 ASCII characters
      3D is “bumpy” code that differentiates by symbol height
        Can be used on metal, hard rubber, other tough surfaces

## Slide 78
Radio-Frequency Identification (RFID)
  Based on an identifying tag bearing a microchip that contains specific code numbers. These code numbers are read by the radio waves of a scanner linked to a database.
  Active RFID tags have their own power source and can transmit signals over a distance to a reader device.
  Passive RFID tags have no battery power of their own and must be read by some sort of scanner.
  RFID tags of both types are used for a wide range of purposes and are starting to replace bar codes in many situations.

## Slide 79
Mark Recognition Readers (source data entry)
  MICR – magnetic-ink character recognition
    Uses special magnetized inks
    Must be read by a special scanner that reads this ink
    Used on bank checks
  OMR – optical mark recognition
    Uses a special scanner that reads
    bubble (pencil) marks
    Used in standardized tests such as the
    SAT and GRE
  OCR – optical character recognition
    Converts scanned text from images (pictures of the text) to an editable text format

## Slide 80
Image-Capture Devices
Digital Cameras
  Use a light-sensitive processor chip to capture photographic images in digital form and store them on a small disk in the camera or on flash memory cards.
    Most can be connected to a PC by USB; smartphones include digital cameras.
  Webcams
    Video cameras attached to a computer to record live moving images then post them to a website in real time.
    Can be attached externally or built into the computer/device.
    Frame-grabber video card
      Can capture and digitize 1 frame at a time
    Full-motion video card
      Can convert analog to digital signals at rates up to 30 frames per second
      Looks like a motion picture

## Slide 81
Digital Camera

## Slide 82
Audio-Input Devices
  Record analog sound and translate it into digital files for storage and processing
  Two ways to digitize audio (often via microphone)
    Sound Board
      An add-on board in a computer that converts analog sound to digital sound, stores it, and plays it back to speakers or amp
    MIDI Board
      Stands for Musical Instrument Digital Exchange
      Uses a standard for the interchange between musical instruments, synthesizers, and computers

## Slide 83
Speech-Recognition Systems
  Use a microphone or telephone as an input device. Converts a person’s speech into digital signals by comparing against 200,000 or so stored patterns.
    Used in places where people need their hands free – warehouses, car radios, stock exchange trades.
    Helpful for people with visual or physical disabilities that prevent them from using other input devices.

## Slide 84
Speech Recognition

## Slide 85
Sensors
  Input device that collects specific data directly from the environment and transmits it to a computer.
  Can be used to detect speed, movement, weight, pressure, temperature, humidity, wind, current, fog, gas, smoke, light, shapes, images, earthquakes, etc.

## Slide 86
Biometric-Input Devices
  Biometrics is the science of measuring individual body characteristics, then using them to identify a person through a fingerprint, hand, eye, voice, or facial characteristics.
  Example: notebook computers equipped with biometric sensors that read fingerprints, instead of passwords, before allowing access to networks.
  Airport and building security systems use biometrics.

## Slide 87: 5.4 The Future of Input

## Slide 88
Data will be input from more and more locations.
Use of source data entry will increase.
  Better input devices for people with disabilities
  Better speech recognition
  Better touch and gesture-recognition input
  Pattern recognition and improved biometrics
  Brainwave input devices

## Slide 89
UNIT 5B: Output Hardware
Softcopy = data shown on a display screen or is in audio or voice form; it exists only electronically. This kind of output is not tangible; it cannot be touched. You can touch disks on which programs are stored, but the software itself is intangible.
Hardcopy = tangible output, usually printed. The principal examples are printouts, whether text or graphics, from printers. Film, including microfilm and microfiche, is also considered hardcopy output.

## Slide 90: 5.5 Softcopy Output
Display Screens

## Slide 91
Features of display screens to consider include screen dimension, screen clarity, and color and resolution standards.
Screen size & aspect ratio
The active display area is the size of a computer screen measured diagonally from corner to corner in inches.
  Desktop computers are commonly 15–30 inches (laptops 12–18 inches, tablets 8.4–14.1 inches, and smartphones 2.5–4.1 inches).

## Slide 92
  The aspect ratio is the proportional relationship of a display screen’s width and height.
    Standard displays have a 4:3 aspect ratio (4 units wide to 3 units high); wide-screen displays have 16:9 or 16:10.

## Slide 93
Screen Clarity
  Dot pitch (dp) is the amount of space between adjacent pixels (square picture elements) on screen.
      The closer the pixels, the crisper the image.
      Get .25 dp or better.
      Resolution refers to the image sharpness.
      The more pixels, the better the resolution.
      Expressed in dots per inch (dpi) .
pixel

## Slide 94
Screen Clarity (continued)
    Color depth (bit depth) is the number of bits stored in a dot (pixel).
      The higher the number the more true the colors.
      24-bit color depth is better than 8-bit color depth, but it needs more video card memory.
  Refresh rate is the number of times per second the pixels are recharged – a higher rate gives less flicker.
Standard bit depths
for color
8-bit—256 colors
16-bit—65,536 colors
24-bit—16,777,216 colors

## Slide 95
  Microcomputers come with graphics cards (video cards) that work with the screen.
  Graphics cards have their own memory (VRAM), which stores each pixel’s information.
  The more VRAM, the higher the resolution you can use.
  Desktop publishers, graphics artists, and gamers need lots of VRAM.

## Slide 96
Types of Display Devices
The most common type of display screens, flat-panel displays are made up of two plates of glass separated by a layer of a substance in which light is manipulated.
One type of flat-panel display is the liquid crystal display (LCD), in which molecules of liquid crystal line up in a way that alters their optical properties, creating images on the screen by transmitting or blocking light.

## Slide 97
  Other types of displays:
Plasma displays: A layer of gas is sandwiched between two glass plates, and when voltage is applied, the gas releases ultraviolet light, which activates the pixels on the screen and forms an image. Although expensive, plasma monitors offer brighter colors and screen sizes up to 150 inches wide; however, they usually do not last as long as other display types.
  Cathode-ray tube (CRT) and others: Falling out of use.
  Multiple screens: Splitting the monitor display area into multiple screens, to view different documents at once.

## Slide 98: 5.6 Hardcopy Output
Printers

## Slide 99
  Printers print text and graphics on paper or other hardcopy materials.
  Printer resolution is measured by dpi (dots per inch); 1,200 x 1,200 is the most common for microcomputers.
  Printers are either impact or nonimpact – impact printers (dot-matrix printer) print by striking the paper directly; nonimpact printers (such as laser printers and inkjet printers) do not have direct contact with the hardcopy medium.

## Slide 100
Like a dot-matrix printer, a laser printer creates images with dots. However, as in a photocopying machine, these images are produced on a drum, treated with an electrically charged inklike toner (powder), and then transferred from drum to paper.
Laser printers run with software called a page description language (PDL) , which tells the printer how to lay out the printed page and supports various fonts.
A laser printer comes with one or both types of PDL: PostScript or PCL (Printer Control Language. In desktop publishing, PostScript is the preferred PDL.
Laser printers have their own CPU, ROM, and memory (RAM), usually 16 megabytes (expandable generally up to 512 megabytes for higher-cost printers).
When you need to print out graphics-heavy color documents, your printer will need more memory.

## Slide 101
Laser Printer

## Slide 102
Inkjet printers spray onto paper small, electrically charged droplets of ink from four or more nozzles through holes in a matrix at high speed.
Like laser and dot-matrix printers, inkjet printers form images with little dots. Inkjet printers commonly have a dpi of 4,800 x 1,200; they spray ink onto the page a line at a time, in both high-quality black-and-white text and high-quality color graphics.

## Slide 103
Inkjet Printer

## Slide 104
Nonimpact printers also include:
  Thermal printers: Low- to medium-resolution printers that use a type of coated paper that darkens when heat is applied to it; typically used in business for bar-code label applications and for printing cash register receipts.
  Thermal wax-transfer printers: Print a wax-based ink onto paper. After it becomes cool, the wax adheres permanently to the paper. Because of their waterfastness, these labels find uses in industrial label printing.
  Photo printers: Specialized machines for printing continuous-tone photo prints , with special paper and color dyes.

## Slide 105
Multifunction printers
  Printers that combine several capabilities:
    Printing
    Scanning
    Copying
    Faxing
  Cost less and take up less space than buying the four separate office machines.
  But if one component malfunctions, so will the other functions.

## Slide 106
Plotters : Designed for large-format printing
  Specialized output device designed to produce large high-quality, 3-D graphics in a variety of colors.
  Used by architects, engineers, and map-makers.
    Pen plotters use one or more colored pens.
    Electrostatic plotters lie partially flat on a table and use toner as photocopiers do.
    Large-format plotters are large-scale inkjet printers used by graphic artists.

## Slide 107: 5.7 MIXED OUTPUT: SOUND, VOICE, & VIDEO

## Slide 108
Mixed Output: Sound, Voice, & Video
  Sound output—produces digitized sounds, even “3-D” sound.
    You need a sound card and sound software.
    Good speakers can improve the sound.
  Voice output—converts digital data into speechlike sounds.
    Used in phone trees, cars, toys and games, GPS systems, and TTS (text-to-speech) systems for hearing-impaired people.
  Video output—photographic images played quickly enough to appear as full-motion.
    Requires powerful processor and video card.
    Video files are large, so a lot of storage is needed, too.
    Videoconferencing is a form of video output.

## Slide 109: 5.8 The Future of Output

## Slide 110
More unusual forms of output
More data used in (Big Data)
More realistic output
  Better and cheaper display screens
  Printers that use less ink
  Movie-quality video for PCs
  Increased use of 3D output

## Slide 111: 5.9 Quality of Life
Health & Ergonomics

## Slide 112
Health Matters
  Overuse injuries and repetitive stress injuries:
    Result when muscle groups are forced through fast, repetitive motions.
    May effect data-entry operators who average 15,000 keystrokes an hour.
    May effect computer users whose monitor, keyboard, and workstation are not arranged for comfort.
    Carpal tunnel syndrome: Caused by pressure on the median nerve in the wrist, through short repetitive movements.
    Eyestrain, headaches, back and neck pains can be problems.
    Electromagnetic fields may be harmful.

## Slide 113
Ergonomics is the methodology of designing a workplace to make working conditions and equipment safer and more efficient.
  Keyboards must be placed at the correct height depending on each worker’s size; detachable keyboards are useful.
  Monitor refresh rates must be fast enough to avoid eyestrain.
  Monitor heights must be correct for comfortable viewing; use a tilting screen.
  Wrist rests may help avoid carpal tunnel syndrome.